## Slide 1
Off-Grid Inverters
SPF 5000 ES Series

## Slide 2
Content
1
Higher Yield
3
Safe & Reliable
2
Smart & Capable
4
Application
www.ginverter.com
CONTENTS

## Slide 3
1
Higher Yield

## Slide 4
Investment
Investment of Off-Gird System
ES Series Inverter:
PV input directly connect to PV terminal (no need install combiner box)
Without battery operating mode (save the investment of battery)
Solar panels in a string and without battery (Save the cost of PV and battery wiring)
SPF 5000 ES
Inverter
Installation
Wire
Battery
Combiner box
(Inverter, solar panel, combiner box, battery, wire, installation)

## Slide 5
Power Factor
Inverter 100% load, still work normally
Over-load 125%, inverter stop working
5KW Power Appliances
5KVA=5KW
5KVA=4KW
Power factor : 1.0
Power factor : 0.8
Output power factor : 1.0 (5KVA=5KW)

## Slide 6
Parallel Operation
Three-phase system
Single-phase system
Parallel operation with up to 6 units only for 4/5KVA, the maximum system output up to 30KW, and also can be set to a three-phase system

## Slide 7
2
Smart & Capable

## Slide 8
Flexibility
1- SE series inverter input range up to 450VDC without
combiner box for PV input.
2- Convenient for installation and save the cost of wiring
and combiner box.
SPF 3000-5000TL HVM
Combiner box
General inverter application Max. PV Input is 145VDC
SPF 5000 ES

## Slide 9
Without Battery Mode
Directly connect solar panel and utility power without battery operation mode
Connect battery for energy storage and back-up support

## Slide 10
3
Safe & Reliable

## Slide 11
SUB Mode
If solar is sufficient ,solar supply power to load, utility will supply power to load at the same time when solar power is not sufficient .

## Slide 12
Battery Discharge Setting
Back to utility mode voltage range: 44-51.2VDC
Setting voltage point back to utility or battery mode:
Utility charging
Battery discharge

## Slide 13
Utility Charging Setting
Setting voltage point back to utility or battery mode:
Back to battery mode voltage range:48-58VDC
Utility charging
Battery discharging

## Slide 14
Battery Equalization
Inverter can setting lead-acid battery equalization charge interval time and charge voltage to active lead-acid battery feature then further can extend lead-acid battery life.
Charging curve

## Slide 15
HMI Operation
Remote monitoring
WIFI, GPRS communication port for remote
monitoring (Supported for 4/5KW)
WIFI-F
GPRS-F
ShinePhone APP
ShineServer

## Slide 16
HMI Operation
1. Input information (PV voltage, AC voltage, frequency, PV generation, battery voltage, charger current)
2. Output information (voltage, load percentage, frequency, load in VA, load in watt, discharging current)
Display screen (Color Display)
PC install monitoring software
SPF 5000 SE
USB cable
PVkeeper monitoring platform

## Slide 17
4
Application

## Slide 18
Enhance Battery Life
Solar power is sufficient
Solar power is not available
Priority mode : Solar first
Solar power is sufficient (Feed to load and also charge the battery). When solar power is not available, Utility supply power to the load and charge the battery

## Slide 19
Save Electricity Bills
Solar power is sufficient
Solar power is not sufficient
Priority mode : SBU first
When Solar power is sufficient (it feeds to load and charge the battery). For cost-effective support, Utility feeds power only if the battery feeding is under low-level warning
.

## Slide 20
Off-Peak Charging
Off-Peak time
Peak time
The time of grid power support and battery discharge can be set during off-peak or peak time